## Slide 1: The RISC-V Hypervisor Extension in gem5
University of Athens, Greece
George-Marios Fragkoulis
Nick Karystinos
D
gem5 workshop @ ISCA 2025
Sunday, 22 June

## Slide 2: Background: RISC-V extensions
The ISA is designed to be extensible and modular
The base ISA provides the “essence” of computation
  1) Basic Arithmetic 2) Control Flow 3) Memory Operations
Optional ISA extensions (“bags” of instructions) provide additional functionality
Each extension is represented by a letter
  A – Atomic Instructions, B – Bit Manipulation, C – Compressed, D – Double Precision fp arithmetic, …

## Slide 3: Background: RISC-V extensions
Why is the ISA designed to be extensible and modular?
RISC-V Mantra: Implement only what you need
  Can tailor the hardware to the application
  Hardware complexity ~ Complexity of ISA extensions needed
  Minimal ISA needs  Simple Hardware 

## Slide 4: Background: RISC-V Hypervisor (H) Extension
H extension allows the efficient hosting of a guest OS
  Essentially: Virtualizes the supervisor-level architecture
Registers
  26 new CSRs
Interrupts & Exceptions
  9 new exception codes (4 new interrupts + 5 new exceptions)
Two-stage Translation
  G-stage Walking for guest physical to host physical translation
Hypervisor Instructions
  20 new instructions including memory fences and special memory instructions for hypervisor

## Slide 5: H extension is now in gem5 
  Pull request is merged onto staging branch of v25.0
Currently testing H extension with Timing CPU models
  Will upstream Timing CPUs support as well (when stable)
This talk High-level overview of the implementation + Demo
Notes: Many thanks to Jason, Roger and everyone else involved for the reviews and insightful feedback

## Slide 6: Implementation
Registers
  26 new CSRs
Interrupts & Exceptions
  9 new exception codes (4 new interrupts + 5 new exceptions)
Two-stage Translation
  G-stage Walking for guest physical to host physical translation
Hypervisor Instructions
  20 new instructions including memory fences and special memory instructions for hypervisor

## Slide 7: Implementation Methodology: Registers
Linux (native – S mode)
Linux (guest – VS mode)
Read sstatus
Read sstatus
csrr t2, sstatus
csrr t2, sstatus
OK!
t2 = sstatus;
OK!

t2 = vsstatus;

## Slide 8: Implementation
Registers
  26 new CSRs
Interrupts & Exceptions
  9 new exception codes (4 new interrupts + 5 new exceptions)
Two-stage Translation
  G-stage Walking for guest physical to host physical translation
Hypervisor Instructions
  20 new instructions including memory fences and special memory instructions for hypervisor

## Slide 9: Implementation Methodology: Exceptions
New fault types
  Virtual Supervisor and Guest Interrupts
  Guest-Page Faults
  Virtual ecall
  Etc.
Extended fault handling for new privileges
  HS (Hypervisor)
  VS (Virtual Supervisor)

## Slide 10: Implementation
Registers
  26 new CSRs
Interrupts & Exceptions
  9 new exception codes (4 new interrupts + 5 new exceptions)
Two-stage Translation
  G-stage Walking for guest physical to host physical translation
Hypervisor Instructions
  20 new instructions including memory fences and special memory instructions for hypervisor

## Slide 11: Background: Sv39 Scheme
VPN2
VPN1
VPN0
offset
L0 PTE
L0 Page Table
L1 PTE
L2 PTE
data
PFN (44 bits)
0
11
12
20
21
29
30
38
9 bits
4KB Page
L1 Page Table
L2 Page Table
satp
9 bits
9 bits
PA
Virtual Address
Physical Address
(Lives in RAM)

## Slide 12: Background: Two-Stage translation
Guest Virtual Address
gPPN2
gPPN1
gPPN0
L0 PTE
L1 PTE
L2 PTE
PFN (44 bits)
hgatp
40
0
11
12
20
21
29
30
G-stage (2nd stage)
Host Virtual Address
VS-stage (1st stage)
gVPN2
gVPN1
gVPN0
offset
L0 gPTE
L0 Page Table
L1 gPTE
L2 gPTE
gPFN (44 bits)
0
11
12
20
21
29
30
38
39-bit Guest Virtual Address
9 bits
4KB Page
L1 Page Table
L2 Page Table
vsatp
9 bits
9 bits
data
Host Physical Address (Lives in RAM)
Guest Physical Address (Host Virtual Address)
Guest Virtual Address

## Slide 13: Implementation
Registers
  26 new CSRs
Interrupts & Exceptions
  9 new exception codes (4 new interrupts + 5 new exceptions)
Two-stage Translation
  G-stage Walking for guest physical to host physical translation
Hypervisor Instructions
  20 new instructions including memory fences and special memory instructions for hypervisor

## Slide 14: Implementation Methodology: Instructions
Extended ISA specification files with the new instruction implementations
  new fences (HFENCE, HINVAL) → selectively flushes TLB entries
  new loads & stores (HLV, HLVX, HSV) → hypervisor accesses memory as if the request originates from a virtualized guest
New memory instruction formats for hypervisor loads & stores

## Slide 15: Implementation Methodology: Validation
Public Tests for H extension
Exceptions & HLV/HSV
Two-Stage Translation
Registers

## Slide 16: Implementation Methodology: Validation
Run a hypervisor and a guest VM
  If the guest VM’s OS boots up and can execute programs
    we gain strong confidence in the correctness of our implementation
We choose to run Xvisor (a type-1 or baremetal hypervisor)
Xvisor Mascot

## Slide 17: Live Demo Time 
Xvisor boot video
QR code points to our CARRV ‘24 paper for more details on the implementation (You can also checkout the PR in the gem5 repository)
Notes: Xvisor boot video

## Slide 18: Thank you! Questions?
University of Athens, Greece
George-Marios Fragkoulis
Nick Karystinos
D
gem5 workshop @ ISCA 2025
Sunday, 22 June

## Slide 19: Background: RISC-V Address Translation
Supports classic paged virtual memory
  different address width translation schemes: Sv32, Sv39, Sv48
  gem5 implements Sv39 (39-bit virtual addresses) for now
H extension adds another translation stage (G-stage)

## Slide 20: Implementation Methodology: Registers
16 bits (HIP CSR)
mtip
0
stip
0
msip
0
ssip
0
seip
0
meip
0
000
…
64 bits (gem5 physical register)
0
1
2
3
4
5
6
7
8
9
10
11
13
15
63
0
12
vssip
vstip
vseip
sgeip
16 bits (MIP CSR)
0
0
0
0
0
0
Additional H extension bits
Original bits
Control Status Register (CSR)
Physical Register
Problem: HIP should see purple bits only
Solution: Read/Write masks nullify the rest
of the bits!

## Slide 21: Experimental Results
We obtain results from nine benchmarks from MiBench Suite
The programs’ full-system execution is simulated in gem5
  Natively (no virtualization)
  In a VM (virtualized environment)
We examine the following three types of simulation overheads
  Simulation Time overhead
  Instruction overhead
  Exception Handling overhead

## Slide 22: Experimental Results: Time Overhead
~50% slowdown on average

## Slide 23: Implementation Methodology: Translation
Extended page walking logic to support new types of walks
  G-stage
  Two-stage
    Virtual First Stage (guest virtual → guest physical)
    G-stage as Second Stage (guest physical → host physical)
Extended permission checking based on effective prv and V
  G-stage accesses are always checked as if prv == PRV_U
  Special Hypervisor memory instructions are executed as if V == true
  New page-fault types (e.g. guest load page fault)

## Slide 24: H extension is now in gem5 
  Pull request is merged onto staging branch of v25.0
We assess the functional correctness of our implementation
  H extension tests behave equivalently on Spike (reference ISA simulator)
  Ran Xvisor (a type-1 hypervisor) and guest VMs
Currently testing H extension with Timing CPU models
  Will eventually upstream Timing CPUs support as well

## Slide 25: Experimental Results: Instructions Overhead
~5% more instructions on average

## Slide 26: Experimental Results: Exceptions Overhead
Exceptions handled in S in native execution and in VS during guest execution
are equivalent

## Slide 27: Background: RISC-V extensions
History of extensions relevant to cloud-computing in gem5 **
[2022] Bit Manipulation (B) Jerin Joy
[2023] Cryptography (K) Roger Chang
[2023] Vector (V) Adrià Armejach, Xuan Hu, Fan Yang, Jerin Joy, Roger Chang, Hoa Nguyen and others
** Excuse the possibly incomplete/mistaken credits 
The missing piece: H (hypervisor) extension Cannot run guest VMs efficiently without this!!!
Notes: What are the “needs” of cloud-computing?

## Slide 28: Background: RISC-V Hypervisor (H) Extension
Firmware
OS
User Space
M
S
1
0
3
U
Firmware
Host User Space
M
1
0
3
U
2
Hypervisor
“Classic” Privilege Levels
With H-extension
HS
Guest User Space
VU
Guest OS
VS
Virtualized Environment
Non-Virtualized Environment

## Slide 29: Thank you! Questions?
University of Athens, Greece
George-Marios Fragkoulis d
George Papadimitriou
Nikos Karystinos
D Dimitris Gizopoulos
CARRV 2024
Sunday, 3 November