## Slide 1: The gem5 Tutorial @HPCA 2024
Presentation by Bobby R. Bruce
Materials designed for gem5 v23.1

## Slide 2: A little about me
2
Started in Sep. 2019
Started as a Postdoc
In Jan 2021 I moved up to being Project Scientist
Spent almost all that time working on the gem5 project.
So, am I an expert in gem5?
Notes: Add Harshil and Ivana here, or just remove this slide.

## Slide 3: What is gem5?
The gem5 architecture simulator provides a platform for evaluating computer systems by modeling the behavior of the underlying hardware. It enables researchers to simulate the performance and behavior of complex computer systems, including the CPU, memory system, and interconnects. This makes it possible to study the performance of different microarchitectural and architectural choices, as well as the effects of different workloads, without having to build and test real systems.
By ChatGPT

## Slide 4: What are we going to cover today?
A short history of gem5.
Getting gem5 setup on your system: Compilation, etc..
Using prebuilt systems.
An overview of event-based simulation and gem5’s software structure
Simulator outputs and how to interpret it.
Creating a system using stdlib components.
Statistical outputs .
SE-mode and FS-mode simulations.
Checkpoints, lower-fidelity components, KVM mode, and Sampling
Creating your own SimObject.
Creating your own stdlib component.
Gem5 Resources.
How to continue to gem5.
Please feel free to speak up!
Discussion is good!
(I don’t have all the answers though!)

## Slide 5: A little bit of history
The m5 Simulator
“A tool for simulating systems”
(~2002)
The GEMS simulator
Provided a detailed memory system.
(~2000)
5
(2011)

## Slide 6: A little bit of history
6
Total Commit*: 21,000
Unique Contributions*: 421
* As of v23.1

## Slide 7: A true public infrastructure project
7
Open Source
Free (like beer)
Massively Collaborative

## Slide 8: Who uses gem5, and why?
8
Education
Academic Research
Industrial R&D

## Slide 9: Education
9
Problem: Students need to learn to design hardware but don’t have a multi-billion-dollar factory

## Slide 10: Academic Research
10

## Slide 11: Academic Researchers
11
We surveyed the top architecture conferences and found:
70% of all computer architecture research utilizes simulation.
The gem5 simulator is by-far the most popular.
Room for improvement: Most users still “roll their own” simulation software. Only 20% use gem5 directly. We want to go above 50% by 2027.

## Slide 12: Industry
12
?
Really, we don’t know exactly. We don’t track users and industrial users seldom make themselves known.

## Slide 13: Industry
13
Big players we know use it

## Slide 14: Let’s hit the ground running
14
This example will show:
How someone obtains gem5.
How you build it.
Running a very basic ”Hello World” simulation.
Getting and compiling gem5 is often the hardest part…
There’s a lot of complicated things happening behind the scenes. I will explain them later.
Notes: Add animation here.

## Slide 15: Typical Downloading
> git clone https://github.com/gem5/gem5
> cd gem5
stable: The default branch for gem5. Updated at stable releases. Currently v23.1.
develop: The branch in which new features, improvements, etc. are added regularly for the next release.
In this tutorial we’re going to use codes paces with a repo which includes some example materials. Though all the gem5 code is v23.1.
15
DON’T DO THIS!

## Slide 16: Using CodeSpaces
Step 1: Go to https://github.com/gem5-hpca-2024/gem5
16

## Slide 17: Using CodeSpaces
Step 2: Click “Code” -> ”Create codespace on stable”
17
Some may be given the option to open this in a local instance of Visual Studio. This is fine. If you receive no option, you’ll run it through the browser. The interface is identical.

## Slide 18: Using CodeSpaces
Step 3: Wait for your environment to load. Then you’re done
18

## Slide 19: Building gem5
> scons build/ALL/gem5.opt –j`nproc`
19

## Slide 20: Let’s start by writing a simulation configuration
20
Open “materials/01-basic.py”. You’ll see the above already prepared for you. Do your work here.

## Slide 21: Let’s be lazy and use a prebuild board
The X86DemoBoard has the following properties:
Single Channel DDR3, 2GB Memory.
A 4 core 3GHz processor (using gem5’s ‘timing’ model).
A MESI Two Level Cache Hierarchy, with 32kB data and instruction case and a 1MB L2 Cache.
Will be run as a Full-System simulation.
Source: “src/python/gem5/prebuilt/demo/x86_demo_board.py”

## Slide 22: Let’s load some software!
(And be lazy again… let’s use something pre-made)
”obtain_resource” downloads the files needed to run the specified workload. In this case the “x86-ubuntu-18.04-boot” workload:
Boots 18.04 with linux 5.4.49
Upon boot will exit the simulation.
https://resources.gem5.org/resources/x86-ubuntu-18.04-boot?version=2.0.0

## Slide 23: The gem5 Resources Web portal
https://resources.gem5.org/resources/x86-ubuntu-18.04-boot?version=2.0.0

## Slide 24: Back to the configuration: Put the board in the simulator
Note: We’re setting “max_ticks” here to stop the simulation after 10 billion simulation ticks. This is just so our simulation stops in a reasonable time `simuator.run()` will have it run to completion.

## Slide 25: There! We’re done!
The completed configuration can be found in “materials-completed/01-basic.py”

## Slide 26: Run the simulation
> ./build/ALL/gem5.opt materials/01-basic.py

## Slide 27: Let’s check other outputs here…
- m5out/
----- board.pc.com_1.device
The terminal output of the simulated system.

## Slide 28: Let’s check other outputs here…
- m5out/
----- board.pc.com_1.device
----- config.{ini/json}
A record of the simulated system in both JSON and INI format.

## Slide 29: Let’s check other outputs here…
- m5out/
----- board.pc.com_1.device
----- config.{ini/json}
----- stats.txt
The gem5 statistic output

## Slide 30: Wait, did we do?
Created a simulation using a pre-built board
Obtained the workload we needed from gem5 Resources
Learned how to clone gem5 and compiled it
Checked the gem5 output files
We…
Set the max tick for the program execution

## Slide 31: Ok, but how does it all work?
Modern systems are very complex, and the design of gem5 simulations reflects this.
However, at its core, the simulator builds on a relatively simple model.

## Slide 32: Nomenclature
Host: the actual hardware you’re using
Running things directly on the hardware: Native execution
Guest: Code running on top of “fake” hardware OS in virtual machine is guest OS Running “on top of” hypervisor Hypervisor is emulating hardware
App
App
Operating Sys.
Hardware
Host
App
App
Operating Sys.
Hardware
Host
Your system
Virtual machines
Hypervisor
Guest

## Slide 33: Nomenclature
Host: the actual hardware you’re using
Simulator: Runs on the host Exposes hardware to the guest
Guest: Code running on simulated hardware OS running on gem5 is guest OS gem5 is simulating hardware
Simulator’s code: Runs natively executes/emulates the guest code
Guest’s code: (or benchmark, workload, etc.) Runs on gem5, not on the host.
App
App
Operating Sys.
Hardware
Host
App
App
Operating Sys.
Hardware
Host
Your system
Simulation
gem5/Simulator
Guest
Workload

## Slide 34: Nomenclature
Host: the actual hardware you’re using
Simulator: Runs on the host Exposes hardware to the guest
Simulator’s performance: Time to run the simulation on host Wallclock time as you perceive it
Simulated performance: Time predicted by the simulator Time for guest code to run on simulator
App
App
Operating Sys.
Hardware
Host
App
App
Operating Sys.
Hardware
Host
Your system
gem5/Simulator
Guest
Simulation
Workload

## Slide 35: At its core: it’s a discrete event simulator
gem5 is a discrete event simulator
Event at head dequeued
Event executed
More events queued
Event - 10
Event Queue
Event - 11
Event - 20
Event - 50
Event - 50
Event - 52
Event - 55

## Slide 36: At its core: it’s a discrete event simulator
gem5 is a discrete event simulator
Event at head dequeued
Event executed
More events queued
Event Queue
Event - 11
Event - 20
Event - 50
Event - 50
Event - 52
Event - 55
Event - 51

## Slide 37: Discrete event simulation example
TIME
Fetch first inst
Send req to cache
Miss in L1, send to DRAM
Put in read Q
L1 tag latency
To DRAM latency
DRAM read latency
Get data from DRAM
Cache recvs data
Processor decodes instruction
Processor executes instruction
Fetch next inst
Response latency
One cycle

## Slide 38: Discrete event simulation
"Time" needs a unit In gem5, we use a unit called "Tick"
Need to convert a simulation "tick" to user-understandable time E.g., seconds
This is the global simulation tick rate Usually this is 1 ps per tick or 1012 ticks per second

## Slide 39: Ok, but how do you schedule these events?
SimObject
Schedule events and process events.
2. Talk to other SimObjects.
While some are incredibly complex, at their core they only do two things:

## Slide 40
This is great, but it takes a lot to get things done
gem5
Config file
This allows for maximum flexibility but can mean creating 100s of lines of Python to create even a basic simulation.

## Slide 41
What is the standard library for?
gem5
Config file
The stdlib is a library which allows for users to quickly create systems with pre-built components.
The stdlib's module architecture allows for components (e.g. a memory system or a cache hierarchy setup) to be quickly swapped in and out without radical redesign.
stdlib

## Slide 42: The stdlib modular metaphor
Processor
Board
Memory
Cache Hierarchy
SingleChannelDDR3_1600
SingleChannelDDR4_2400
...
Simple Processor
SwitchableProcessor
...
No Cache
PrivateL1PrivateL2
MesiTwoLevel
...

## Slide 43
Let’s build using components!
Open “materials/02-components.py” You’ll see the above already prepared for you.

## Slide 44
Let’s choose a cache hierarchy and memory system

## Slide 45
And a processor!
The SimpleSwitchingProcessor allows for different types of cores to be swapped during a simulation with `processor.switch()`.
This can be useful when wanting to switch to and from a detailed form of simulation. More on this alter.

## Slide 46
Then let’s plug them into a board
We add the components to the board, in this case an `X86Board`.

## Slide 47
Load in our workload to the board
The `set_kernel_disk_workload` function accepts a kernel binary resources and a disk images resources.
In addition, here we are passing a command via the `readfile_contents` parameter which will run after the boot is complete.
The `m5 exit` command will exit the simulation loop.

## Slide 48
Simulated System
Run the simulator
Boot OS
`readfile_contents` executed
1st `m5 exit`
`echo ”This is…”`
`sleep 1`
2nd `m5 exit`
End of Simulation

## Slide 49
Run the simulator
> ./build/ALL/gem5.opt materials/02-components.py
A completed version of the configuration can be found in “materials-completed/02-01-components-initial.py”

## Slide 50
We can do better…
Here we can specify exactly what to do on each exit event type via Python generators.
The Simulator had default behavior for these events, but they can be overridden.
ExitEvent.EXIT
ExitEvent.CHECKPOINT
ExitEvent.FAIL
ExitEvent.SWITCHCPU
ExitEvent.WORKBEGIN
ExitEvent.WORKEND
ExitEvent.USER_INTERRUPT
ExitEvent.MAX_TICK

## Slide 51
To run
> ./build/ALL/gem5.opt materials/02-components.py
This will take a while to run but you can see the terminal output in “m5out” while this is running.
Cntr+C to exit the simulation.

## Slide 52: What did we just do?
A “full-system” simulation
Created and handled exit events
Switch CPU fidelity at a chosen point
Dumped Statistics for our chosen ROI
The simulations so far are so slow…

## Slide 53: gem5 is slloooww
Simulating 1 Second
>> 100k seconds on the host
(Not our fault: It’s the natural of simulation)

## Slide 54: Fortunately, there are some work arounds
Simulation Fidelity
Simulation Time
Key idea: You don’t need to simulate everything perfectly, or at all.

## Slide 55: Simulations can always be made faster by simulating less

## Slide 56: This isn’t always a bad thing… a lot of a simulation is of no interest to us
Kernel Boot
Wider OS setup
Benchmark application load
ROI
Finish and cleanup
🥱🥱🥱
👀 👀

## Slide 57: Some techniques we provide
CPU Models
KVM Mode
Checkpoints
Sampling: Simpoints and Loopoints
SE Mode

## Slide 58: SE mode vs FS mode
Host System
Full-System Simulation
Hardware
OS
Application
Host System
Syscall Emulation Simulation
Hardware
OS
Application
SE Mode relays application syscalls to host OS. This means we don’t need to simulate an OS for applications to run
In addition, we can access host resources such as files of libraries to dynamically link in.

## Slide 59: SE mode example
SE Mode
A pre-made script which uses SE-mode can be found in “materials/03-se-mode.py”.
It’s very similar to the scripts you’ve created thus far but uses the `SimpleBoard`.
Let’s try to understand the script first before demoing SE Mode. It includes some features we’ve yet to explain.

## Slide 60: Suites (and argparse)
Notes: Expand here looking up suites on the website, how you can see their contents, etc.

## Slide 61: The require function: Making sure we built the right thing
Notes: Add more here about the other things we can declare in the `requires` function.

## Slide 62: SE mode
> ./build/ALL/gem5.opt materials/03-se-mode.py \
arm-matrix-multiply-run
This will take about a minute to run.
This would’ve taken hours to run in FS, but in SE ignore the entire OS simulation
You can try other CLI options too.

## Slide 63: FS and SE mode: Common Fit falls
“FS mode takes too long so I just switched over to SE mode”
You must understand what you’re simulating and whether it’ll impact results.
”gem5 Won’t let me run a binary with elevated instructions”
SE-mode will only allow you to simulate user-space instructions. We can’t just pass elevated instructu
”I can’t run my program in SE-Mode because a syscall isn’t implemented correctly”
We’d love to have all the syscalls implemented but it’s too much work.

## Slide 64: FS and SE mode
FS mode does everything SE mode does, and more! When in doubt, or struggling with SE, use FS mode.

## Slide 65: CPU Models
CPU Models
Memory Accesses
How memory are simulated
Timing
Atomic
CPU Design
The type of CPU design. The simpler the faster.
O3
Pipeline
Simple
Notes: Show changing TIMING to atomic in our example and how that may improve things.

## Slide 66: CPU Models: Memory Accesses
CPU Models
Atomic Accesses
When a memory is accessed, the CPU gets the data instantly and latency is simply estimated for statistics. I.e., everything is happening in one function call from the CPU, in a single event in the Queue.
Low fidelity but fast!
Only suitable if you don’t care about memory access data (kind of rare for computer architects…).
Notes: Show changing TIMING to atomic in our example and how that may improve things.

## Slide 67: CPU Models: Memory Accesses
CPU Models
Timing Accesses
Memory requests are responded to by scheduling events in the future in the event queue.
I.e., a request is made by the CPU to memory and the response is scheduled in the event queue.
Low but more accurate.
Notes: Show changing TIMING to atomic in our example and how that may improve things.

## Slide 68: CPU Models: Simple
CPU Models
Simple CPU
A basic in-order CPU model. Due to its relative simplicity, it is relatively easy to simulate compare to other CPU model types.
Notes: Show changing TIMING to atomic in our example and how that may improve things.

## Slide 69: CPU Models: Simple
CPU Models
Minor CPU
A CPU model for simulating pipelines. The Minor CPU is highly configurable.
Notes: Show changing TIMING to atomic in our example and how that may improve things.

## Slide 70: Let’s play around with a few different CPU models
Go back to the “materials/03-se-mode.py script.
Try changing the `cpu_type` field of the `SimpleProcessor` and see how it impacts simulation execution time (see ‘host seconds; in “m5out/stats.txt” for this information
A Simple CPU using the Timing memory access model.
A Simple CPU using the Atomic memory access model.
A O3 CPU using the Timing memory access model.

## Slide 71: What I observed with matrix-multiply
Chart: Seconds taken to complete execution of Matrix-Multiply
Atomic | 8
Timing | 44
O3 | 110

## Slide 72: KVM Mode: The other special CPU Type
Due to GitHub Codespace restrictions, we cannot use this special CPU type.
If you later wish to check your host system’s compatibility and how to setup KVM see: https://www.gem5.org/documentation/general_docs/using_kvm/
The KVM CPU utilizes the host systems Kernel Virtual Machine to utilize the host hardware to execute instructions.
The host must have KVM enabled and be of the same ISA type as that being emulated.
KVM always runs with Atomic memory accesses. It is simulating almost nothing and is therefore very fast.
Notes: Demo KVM mode (if I can)

## Slide 73: Checkpointing
Checkpointing allows for a simulation to save its state then load to that state later.
This is useful in cases where you want to quickly jump to points in .
This is literally like a checkpoint/save in a video game.
The simulated system that restores the checkpoint can differ from that which created it. There are some restrictions:
1. You can’t restore to a system with less memory.
2. You can’t restore with a different workload.
3. Ruby Cache Hierarchy’s are wiped. Ergo you start with a clean cache from restore.

## Slide 74: Saving a Checkpoint
Open “materials/04-01-saving-a-checkpoint.py”.
Let’s first go through the file to understand what this configuration is doing.

## Slide 75: Saving a Checkpoint
This is a function definition in “src/gem5/python/simulate/simulator.py”. Using this info, append to the configuration file to make it create a checkpoint after the first `m5 exit`.
When done, run the script. It should take about 20 minutes.

## Slide 76: Saving a Checkpoint
Don’t worry, I’ve created one for you: “materials-completed/checkpoints/04-01-saved-checkpoint”

## Slide 77: Restoring from a checkpoint
Open “materials/04-02-saving-a-checkpoint.py”.
Again, let’s go through this file. Note the differences.
This file is complete. Run it and see the restore in action.

## Slide 78: Sampling!
Sampling
Right now, a bit experimental.
Advanced users only!
Sampling is only simulating small parts of an execution then extrapolating data from there.
SimPoint and Looppoint are partially integrated into gem5.
There are some toy examples in “configs/example/gem5_library/looppoints”.

## Slide 79: You can now
Setup simulations
using the gem5 stdlib
Use Exit Events to return data and alter parameters at specific points in time
Reduce your simulation time with a set of tricks to lower and increase fidelity
Understand Event-based Simulation
Obtain, compile, and run gem5
Understand SE and FS mode

## Slide 80: What’s next?
While we strive to provide a tool which allows for easy simulation of typical hardware setups via modular connections between components provided by the project…
Research and development requires creation of something new. We must therefore know how to create new components, SimObjects, and incorporate them into our designs.
We provide you with 99% of a simulated system so you can fuss over that 1% that’s unique to your project

## Slide 81: SimObjects at a glance
Model C++ code in src/
Parameters Python code in src/ In SimObject declaration file
Instance or configuration A particular choice for the parameters In standard library, your extensions, or python runscript

## Slide 82: Adding a new SimObject
Step 1: Create a Python class (SimObject description file)
Step 2: Implement the C++
Step 3: Register the SimObject and C++ file
Step 4: (Re-)build gem5
Step 5: Create a config script

## Slide 83: Adding a new SimObject
Create a new directory in “src” called ”simobject-example”.
All the files will go there.

## Slide 84: Step 1: Create a Python class
| from m5.params import *
| from m5.SimObject import SimObject
|
| class HelloObject(SimObject):
| type = ”HelloObject"
| cxx_header = ”simobject-example/hello_object.hh"
| cxx_class = "gem5::HelloObject"
Import the objects we need
m5.params: Things like MemorySize, Int, etc.
type: The C++ class name
cxx_header: The filename for the C++ header file
HelloObject.py
cxx_class: The fully qualified C++ class name

## Slide 85: Step 2: Implement the C++
| #include "params/HelloObject.hh"
| #include "sim/sim_object.hh”
| namespace gem5{
| class HelloObject : public SimObject
| {
| public:
| HelloObject(const HelloObjectParams &p);
| };
| } // namespace gem5
hello_object.hh
params/*.hh generated automatically. Comes from Python SimObject definition
Constructor has one parameter, the generated params object. Must be a const reference

## Slide 86: Step 2: Implement the C++
#include ”simobject-example/hello_object.hh”
#include <iostream>
Namespace gem5 {
HelloObject::HelloObject(const HelloObjectParams &params) : SimObject(params)
{
std::cout << "Hello World! From a SimObject!" << std::endl;
}
} //
hello_object.cc

## Slide 87: Step 3: Register the SimObject and C++ file
| Import('*')
| SimObject(HelloObject.py', sim_objects=[HelloObject'])
| Source(hello_object.cc')
SConscript
Import: SConscript is just Python… but weird.
SimObject(): Says that this Python file contains a SimObject. Note: you can put pretty much any Python in here
Source(): Tell scons to compile this file (e.g., with g++).
sim_objects: The SimObjects declared in the file (could be more than 1)

## Slide 88: Step 4: (Re-)build gem5
> scons build/ALL/gem5.opt –j`nproc`

## Slide 89: Step 5: Create a config script
> build/ALL/gem5.opt run-hello.py
...
Hello world! From a SimObject!
...
| import m5
| from m5.objects import *
| root = Root(full_system=False)
| root.hello = HelloObject()
|
| m5.instantiate()
| exit_event = m5.simulate()
| print(f"Exiting @ tick {m5.curTick()} because" | "{exit_event.getCause()}")
Instantiate the new object that you created in the config file (e.g., simple.py)
All simulations require a Root
Instantiate all the SimObjects (create the C++ instances)
Simulate the system as configured!
Notes: Not there’s a completed example here under “materials-completed/05-creating-simobject"

## Slide 90: Adding Parameters and events to the SimObject
Add this to “HelloObject.py”.
This declares the parameters of the SimObject.

## Slide 91: Adding Parameters and events to the SimObject
Update the “hello_object.hh” with the parameters and the event variables/functions.
The “processEvent” function will handle the event.
The “event” variable will wrap the “processEvent’ function.
The other variables store the stage of the object and the variables

## Slide 92: Adding Parameters and events to the SimObject
Now we updated ”hello_object.cc” to set the variables and functions.
We’ve also changed the `std::cout` to output the Object name.

## Slide 93: Adding Parameters and events to the SimObject
Implement the `startup` and `processEvent` functions in ”hello_object.cc”
The `startup` schedules the event before the simulation starts with ‘latency`.
The `processEvent` will continue to reschedule the event `timeLeft` times.

## Slide 94: Adding Parameters and events to the SimObject
Because `time_to_wait` does not have a default value we must set it in the config script.
Add this to your run script.

## Slide 95: Adding Parameters and events to the SimObject
scons build/ALL/gem5.opt –j`nproc`
./build/ALL/gem5.opt <your run script>
After, why don’t you try running changing the default `number_of_fires` parameter to something more interesting.

## Slide 96: A little more to do in your own time
https://www.gem5.org/documentation/learning_gem5/part2/parameters/ contains an additional part of this tutorial which involves adding another SimObject: “GoodbyeObject” which schedules a Goodbye event when the HelloObject events cease scheduling
If your interested in SimObjects and creating your own this is worth doing..

## Slide 97: Let’s see how SimObject objects are configured, utilized and create new components
Let’s do it live! Try to follow along!
(an example can be found in “materials-completed/07-our-silly-cache”)

## Slide 98: gem5 Resources
A resources is something that runs on a simulated system.
While the underlying simulated hardware remains the same, what resources are used in the simulation impact what the simulated system runs and how the simulator runs it.
Typically, this is software, disk images, or data to be loaded into the simulated system’s memory/storage.
It may also be things like “checkpoints” for the simulation to use, or sampling data.
They are files, directories, programs, and generally thing that doesn’t impact a simulated configuration but does impact it’s running.

## Slide 99: Contributing to gem5
You’ve learned a thing or two about gem5, why not work to make it better?

## Slide 100
Our Strategy
Learn
Use
Develop
Contribute
Improve
More interest
Notes: We want to teach people how to use gem5 so they use gem5.
People who use gem5 will want to extend gem5.
We hope those people who create useful extensions will contribute
Learn -> Use -> Develop -> Contribute -> Make gem 5 better -> More interest -> Learn

## Slide 101
Why should I contribute to gem5?
You’re Nice!
You’ve found a bug and have a fix.
You’ve developed something useful and want to share it.
Fame!
Looks good on your CV.
Companies contribute to gem5 all the time.
Fortune!
Get yourself known in the project.
Good PR for your research to have it incorporated in gem5.
Notes: You want to be a good citizen
  You’ve found a bug and have a fix.
  You’ve got a useful feature you think will be of benefit.
Fame
  Looks good to have contributed to an open source project.
  Some cool architectural concept will get more interest in the community if they can be easily simulated in gem5
Fortune
  Your company may use gem5 as a critical tool, by engaging in development you can make your company better.

## Slide 102
“I’m scared”
Understandable…
Very few patches get in straight away. Most patches are only accepted after requests for changes.
We try our best to keep feedback as constructive as possible (don’t take it personally!).
The purpose of this session is to make it less scary!
Notes: Yes, it’s scary
Very few patches get in “straight away”, most patches submitted will receive feedback and requests for changes before accepting them
We try our best to keep negative feedback as constructive as possible
The purpose of this session is to make it all less scary for you.

## Slide 103
What can I contribute?
Your own changes (bug fixes are very welcome!)
Check the GitHub Issue Tracker:
https://github.com/gem5/gem5/issues
Notes: Your own changes (bug fixes very welcome)
Check the Jira
Some things we’re always needing more of:
More tests!
Incorporation of Syscalls for SE mode
Unimplemented ISA instructions/extensions
Useful stdlib components
Useful gem5 resources

## Slide 104
What can I contribute?
Some stuff we’re always needing more of:
Tests
Incorporating Syscalls for SE mode
Unimplemented ISA instructions/extensions
Useful stdlib components
Useful gem5 resources
Updating documentation on the gem5 website
  Even fixing typos is helpful!
Notes: Your own changes (bug fixes very welcome)
Check the Jira
Some things we’re always needing more of:
More tests!
Incorporation of Syscalls for SE mode
Unimplemented ISA instructions/extensions
Useful stdlib components
Useful gem5 resources

## Slide 105
What can’t I contribute?
3,.It’s dangerous
You’ve changed a lot of code and haven’t proven you’ve not yet broken anything. Tests are required at a minimum.
Anything that’ll burden the community with too much maintenance overhead.
Yeah, you’ve developed something nice for us, but it’s big and complex: are you going to stick around to help us maintain it? Is it engineered for that to be easy?
2. Something overly niche and lacks general applicability
The component you made to carry out your research may be interesting to you but adding it to the codebase may just be bloat to most users: Consider sharing such things on your own git repos.
3. It doesn’t confirm to our standards
The code appears fine, but you’ve not conformed to our style guide.
Notes: Your own changes (bug fixes very welcome)
Check the Jira
Some things we’re always needing more of:
More tests!
Incorporation of Syscalls for SE mode
Unimplemented ISA instructions/extensions
Useful stdlib components
Useful gem5 resources

## Slide 106
Forking and cloning
Step 1: Go to https://github.com/gem5/gem5
Step 2: Fork the repo
Step 3: Clone the forked repo
Notes: Note: They don’t need to clone and explain why switch from develop then “my-change” is necessary.

## Slide 107
Where do I make changes?
>git switch develop
>git switch –c my-change
Notes: Note: They don’t need to clone and explain why switch from develop then “my-change” is necessary.

## Slide 108
Making changes: CPP
Full style guide here: https://www.gem5.org/documentation/general_docs/development/coding_style/
High-level overview: https://www.gem5.org/contributing#making-modifications
Doxygen is highly recommended
http://doxygen.gem5.org
Notes: Discuss here an example to make a CPP file, emphasize the style guide and point towards resources.
Discuss leaving a comment and the Doxygen website

## Slide 109
Making changes: Python
> pip install black
> black <python file>
For variable/method/etc. Naming conventions please follow the PEP 8 naming convention recommendations: https://peps.python.org/pep-0008/#naming-conventions
While we try to enforce naming conventions across the gem5 project, we are aware there are instances where they are not.
In such cases please follow the convention of the code you are modifying.
Notes: Discuss here an example to make a Python file, emphasize the style guide, show how to make good comments.

## Slide 110
The biggest gotchas!
Whitespace at the end of a line.
Indentation not 4 space characters (please, no tabs)
Lines too long (for CPP, no more than 79 characters!)
When in doubt, follow the style around you!
We have a style checker which should stop you committing if you’ve done something wrong, but it’s not perfect and can be side-stepped.
Notes: Discuss here an example to make a Python file, emphasize the style guide, show how to make good comments.

## Slide 111
Ensure pre-commit is installed
> ./util/pre-commit-install.sh
Pre-commit ensures when you are about to commit a change a series of checks are run on your code to ensure it conforms to our style guide
Notes: Discuss here an example to make a Python file, emphasize the style guide, show how to make good comments.

## Slide 112
Using git
> git add <files to add>
> git commit

## Slide 113
Commit message rules
We have some unique rules for gem5:
The header must lead with tags (see MAINTAINERS.yaml for a list of tags).
Headers should be clear, short descriptions of what a patch will do.
Headers should be no longer than 65 characters
A blank line separates the header and the patch description.
Descriptions can span multiple paragraphs, but lines should not exceed 72 characters (this is lax rule, it’s acceptable to exceed this if you’re quoting code, or including a URL).

## Slide 114
View the Git Log
> git log

## Slide 115
Example commit message

## Slide 116
How do I push?
> git push
This pushes to your forked repo

## Slide 117
Create a pull request
Select the branch you just pushed

## Slide 118
Create a pull request
Click “Open Pull Request” under “Contribute”

## Slide 119
Create a pull request
Fill out the form. Of note: Change the base branch to “develop”.
Once filled, click “Create Pull Request”

## Slide 120
Pull Request waiting for testing and review
https://github.com/gem5/gem5/pulls

## Slide 121
PR Review Process
PR Created
Tests Pass?
Update change
Wait for Tests to complete
Yes
PR Merged
PR is reviewed by community member.
Suggestions made
Yes
No
Maintainer Decides if to merge Change
Approve
Refuses (rare)
To make changes just push to your forked repo branch!
Notes: Your own changes (bug fixes very welcome)
Check the Jira
Some things we’re always needing more of:
More tests!
Incorporation of Syscalls for SE mode
Unimplemented ISA instructions/extensions
Useful stdlib components
Useful gem5 resources

## Slide 122
Testing overview
Compiler Tests (Run Weekly)
Daily Tests
Weekly Tests
CI Tests
Execution time
Badges are shown on the repo main page: https://github.com/gem5/gem5?tab=readme-ov-file#testing-status
The most direct are the “CI Tests”, you cannot merge your change into develop without these passing on your PR.
The rest run either daily or weekly. It is therefore possible your PR breaks gem5 but there’s a delay in us finding out (so keep an eye on these tests).
Notes: Your own changes (bug fixes very welcome)
Check the Jira
Some things we’re always needing more of:
More tests!
Incorporation of Syscalls for SE mode
Unimplemented ISA instructions/extensions
Useful stdlib components
Useful gem5 resources

## Slide 123
What about the other gem5 repos?
gem5 Resources
https://github.com/gem5/gem5-resources
The Sources for the gem5 Resources
Build atop “stable” to make changes for the current release.
Built atop “develop” to make changes for the upcoming release.
gem5 Website
https://github.com/gem5/website
The www.gem5.org sources.
Changes made to the “stable” branch are live.
Changes made to “develop” will be merged into stable on the next gem5 release.
Neither of these are held up to the same standards as the gem5 repo but changes to them are reviewed.

## Slide 124
Some useful resources
https://www.gem5.org/contributing
CONTRIBUTING.md in the gem5 directory
Sometimes using git is the biggest hurdle:
https://git-scm.com/book/en/v2 : The git book
https://dev.to/milu_franz/git-explained-the-basics-igc : I think this is a good tutorial but is very GitHub-centric (we don't use GitHub for gem5). Still, going through it would be beneficial.
https://wiki.spheredev.org/index.php/Git_for_the_lazy : Does a quick run through of the basic Git commands. Can be good for reference.
http://marklodato.github.io/visual-git-guide/index-en.html: A bit more complex but tries to introduce the git data structures involved in git
https://towardsdatascience.com/git-help-all-2d0bb0c31483: Another resource outlining both the commands and explaining how git works.

## Slide 125: Caveats
gem5 is a tool, not a panacea
Most models are not validated against “real” hardware
“All models are wrong but some are useful”
See “Architectural Simulators Considered Harmful”by Nowatzki et al. (2015).
There are bugs!

## Slide 126: Bobby’s Advice
Learn git. By that, I mean beyond “git add” and “git commit”.
Get comfortable with Object Oriented design. The gem5 codebase depends heavily on it. Learn it and incorporate it in your work.
Don’t modify, extend! Hacking what’s already there will cause problems. Create new SimObjects, components, scripts as needed.
Understand the data you need before trying to make gem5 go faster. SE mode, checkpoints, faster CPU models etc. are tempting but they have trade-offs.
Do not configure your system via the command line: Configurations exist in your configuration file and associated components, SimObjects, etc.

## Slide 127: References
Martin et al. 2005. Multifacet’s general execution-driven multiprocessor simulator (GEMS) toolset. ACM SIGARCH Computer Architecture News. https://doi.org/10.1145/1105734.1105747
Binkert et al. 2006. The M5 simulator: Modeling Networked Systems. IEEE Micro. https://doi.org/10.1109/MM.2006.82
Binkert, et al. 2011. The gem5 simulator. SIGARCH Comput. Archit. News 39 http://dx.doi.org/10.1145/2024716.2024718
Lowe-Power et al 2021. The gem5 Simulator: Version 20.0+. ArXiv Preprint ArXiv:2007.03152, 2021. https://doi.org/10.48550/arXiv.2007.03152
Nowatzki et al. 2015. Architectural simulators considered harmful. IEEE Micro. https://doi.org/10.1109/MM.2015.74